## Slide 1: UD OpenACC Hackathon Team NCI CBIiT
George Zaki, Eric Stahlberg
Mentor: Peng Wang

## Slide 2: RNA Structure Optimization with Xray Data
Knowing RNA structure is key to understanding biology
Knowing structure means to potentially impact dependent proteins
Application uses Small angle Xray Scattering data to optimize RNA structure
Compare theoretical scattering profile to actual scattering profile
Adjust RNA geometry until a match is achieved
Application uses simulated annealing in a constrained optimization of molecular geometry

## Slide 3
Reduction loop takes 80% of the time.
Host to Device memcpy of small arrays ~600 doubles
Outer loop 61 iterations
Reduction is performed using two inner loops accessing the upper triangle matrix:
for (int i=0; i<61; i++){ red = 0; for ( j = 1; j <= natoms ; j++){ for ( k = j+1; k <= natoms ; k++){ .... red += ...; }

## Slide 4: Open_ACC First Pass Profile
Map i loop to Blocks
Flatten inner loops and retrieve indexes:
for (int iter = 0; iter < nadditions; ++iter) { int j = natoms - 2 - int(sqrt(-8*iter + 4*natoms*(natoms-1)- 7)/2.0 - 0.5); int k = iter + j + 1 - nadditions + (natoms-j)*((natoms-j)-1)/2; j++; k++; ....... red += ... }

## Slide 5: NVProf

## Slide 6: TASks
Explore CUDA implementation to have a tighter contral of array to memory mapping
Investigate scaling up the code to 2GPUs.
Identify other hot spots in the application.

## Slide 7: Particle Tracking of Molecular RNAs
Knowing the location and interactions of RNA in a cell are key to understanding biology
RNA transcription sites are identified with fluorescing molecules
Need to match successive frames of multi-cell image movies to track individual transcription sites
Currently done manually. Seeking to automate.